## Slide 1: Vectorized Emulation
Buckle up!

## Slide 2: About me
Hello, my name is Brandon Falk
Twitter is my best contact @gamozolabs
  I also stream under `gamozolabs` on YouTube and `gamozo` on Twitch
    Sometimes I make actual videos, would love to do more
  And I write blogs at https://gamozolabs.github.io
I write a lot of exotic harnesses and fuzzers
  Multiple hypervisors and operating systems for fuzzing
  Emulators and JITs
  Using 0-days and heavy reversing to snapshot closed-source systems
    Even systems without public binaries
CPU vulnerability research (found MLPDS, wrote PoCs for almost every CPU bug)

## Slide 3: Public Information on Vectorized Emulation
Introduction to the concept
  Talk through the high-level goals of vectorized emulation
  https://gamozolabs.github.io/fuzzing/2018/10/14/vectorized_emulation.html
MMU Design
  Talking about how the MMU was designed for high-performance vectorized JIT
  https://gamozolabs.github.io/fuzzing/2018/11/19/vectorized_emulation_mmu.html
“Solving” behavior
  Discuss the benefits of vectorized emulation and how it explores the unknown
  Blog scheduled for a later date

## Slide 4: Terminology
Term | Meaning
Vector | Register containing multiple pieces of data
Lane | One single component of a vector
VM / Guest | Virtual machine, broadly used to refer to an emulated or virtualized guest. This guest has it’s own register and memory state that’s kept in an isolated environment.
Parallel | Performing the same operation on multiple pieces of data in a vector
Neighbor | Lane of another VM which is executing along side of another lane. 16 VMs execute per vector, thus each VM has 15 “neighbors”

## Slide 5: What is vectorized emulation?
Emulation of multiple VMs in parallel on a single hardware thread using Intel AVX-512 instructions
Gather code coverage, memory coverage, and register coverage
  Divergence/differential reduces coverage overhead
Better-than-ASAN memory protections
Perf hit due to emulation? Nope… actually faster than native
  Typically 30% faster than native with full coverage, 2-3x without coverage
  2 trillion emulated instructions per second (raw math targets)
  100 billion emulated instructions per second (“standard” targets)
  (Benchmarks from a $2k USD 64 core Knights Landing 7210)

## Slide 6: Agenda
Vectorization/SIMD
  What is it?
  Why is it part of ISAs?
Snapshot fuzzing
  How does it differ from “traditional” fuzzing?
  What are the benefits?
Vectorized emulation
  How do we leverage vectorization for emulation?
  What does it mean for fuzzing?
Results
  Does this actually work?

## Slide 7: SIMD / Vectorization
A primer on SIMD

## Slide 8: Single instruction, multiple data (SIMD)
MMX/SSE/AVX on x86, NEON on ARM, AltiVec on PPC, etc
One instruction performs the same operation on multiple inputs
SIMD instructions are typically the fastest way to process data on a CPU
These are the “gross” instructions you run into when reversing
  `vpcmpestri`, `vpshufbitqmb`, easy on the eyes
Typically only used in math-intensive operations and research
Also useful for memory operations, `mem*()`, `str*()` libc routines

## Slide 9: SIMD introduction to x86 (MMX)
Started with MMX in 1997
Added 8 new 64-bit registers, mm0-mm7
mm registers could hold one 64-bit integer, two 32-bit integers, four 16-bit integers, or eight 8-bit integers
Packed operations could be performed on the different “lanes” in parallel
  The lanes are the packed smaller-than-register integers
Only integer operations with original MMX

## Slide 10: Example: Adding with MMX
Packed adds can be performed with the `padd` instructions
  paddb – Packed add bytes (8 x 8-bit operations)
  paddw – Packed add words (4 x 16-bit operations)
  paddd – Packed add double-words (2 x 32-bit operations)
  paddq – Packed add quad-words (1 x 64-bit operation)

## Slide 11: Example: paddw mm0, mm1
5
6
8
7
mm0
1
2
4
3
mm1
+
6
8
12
10
mm0
=

## Slide 12: Why SIMD?
Performance speedup
Fewer instructions to decode
Fewer dependencies to track
  All the packed adds are independent and ordering doesn’t matter
Users
  Media encoding/decoding (images, video, sound, etc)
  Rendering and graphics
  Neural nets
  Finance
  … really anything with multiple streams of data to perform the same math on

## Slide 13: Modern SIMD on Intel x86
SSE (1999), 8 x 128-bit registers, packed float support
  SSE2, SSE3, SSSE3, SSE4, etc: More complex instructions added
AVX (2008), 16 x 256-bit registers
AVX-512 (2013), 32 x 512-bit registers
  Added support for kmask registers
  Neural-net specific instructions
  Whopping 512 single-precision floats storable in each thread’s register file

## Slide 14: Scalar vs AVX-512 performance
add eax, [rsp + 0x00]
add ecx, [rsp + 0x04] add edx, [rsp + 0x08]
add ebx, [rsp + 0x0c]
…
add r15d, [rsp + 0x3c]
vpaddd zmm0, zmm1, zmm2
2 instructions per cycle
1 instruction total
0.5 cycles total
No memory access needed, data fits in register file
1 instruction per cycle
16 instructions total
16 cycles total
Memory accesses required due to large amounts of state (16 dwords)

## Slide 15: Real-world SIMD
Handwritten using intrinsics for high-performance programs
  Intrinsics are 1-to-1 C/C++ implementations of assembly instructions
  For example: _mm_aesenc_si128(x, y) will generate an `aesenc` instruction
  Allows using high-level languages like C to write assembly-level optimizations
Often automatically generated by your compiler
  Not too great compared to handwritten
  Frameworks like OpenCL can be used to help write C and benefit from CPU/GPU scaling

## Slide 17: Snapshot Fuzzing
Deterministic and focused fuzzing

## Slide 18: Snapshot Fuzzing
Fuzz cases start with memory and register state
Registers and memory are reloaded to the saved state
User-controlled inputs are modified in memory
Execution is resumed from this snapshotted point
When a fuzz case ends, the state is restored
  Often differentially, where only modified memory is restored

## Slide 19: Why Snapshot Fuzzing?
Skip application startup times
Allows for easier emulation of hard-to-emulate targets
  Take a snapshot on an iPhone, continue execution in emulation
Fully deterministic, or at least higher levels of determinism
  Application continues from the same state each fuzz case
  Same fuzz input should give the exact same result
Comparing different inputs to the same snapshot is an apples-to-apples comparison
  Any difference in execution is due to the user input, not unknown program state

## Slide 20: Determinism
My #1 priority, even if there’s a performance regression
Same input should produce the exact same result
  Same memory accesses, register values, program flow, etc
Never have a crash that cannot reproduce
Any new coverage is due to the change made in the input
  The only variable is the input to the program, all other state is constant
Easier to A-B test fuzzer performance
  Modify fuzzer, see if it gets crashes faster or more coverage
  If it did, the change made to the fuzzer were likely an improvement

## Slide 21: Snapshot Fuzzing Difficulties
Not always easy, per-target harnessing to take a snapshot
  Sometimes an 0-day is required to take a snapshot, especially on locked-down devices
Snapshot must be “atomic”, memory cannot be changing during snapshotting
Custom devices may need to be emulated
Higher upfront cost, lower fuzz costs
Honestly… never really had a problem doing snapshot fuzzing on a wide variety of targets

## Slide 22: Real-world example
Snapshot fuzzed Word RTF in 2013 using falkervisor
Reversed where Word loaded up files
  Had some C++ class which cached accesses to files
Placed breakpoint after first NtReadFile() which read the input file
When breakpoint is hit, all of physical memory and register state is saved
This state is re-created in a new VM when fuzzing
Input just read from disk is modified in memory
Fuzzer runs until termination (timeout, crash, parsing complete, etc)
VM is reset differentially to the original state, and a new case starts!

## Slide 23: Real-world Results
4,000 fuzz cases per second fuzzing Word on a 64-core machine
Deterministic crashes
  All bugs reproduced and thus triage was much easier
Inputs could be automatically minimized
  Randomly delete sections of bytes from the input file
  Same crash? Save the new input, continue
  No crash, different crash? Revert to the last-known-crashing input
  250 KiB input RTFs minimized down to 50-80 bytes in 15-20 seconds
Over 30 unique bugs, 10+ RCE bugs
  Spent most human time doing triage
  About 30-40% of the bugs lasted for more than 5 years

## Slide 24: Vectorized Emulation
The concept, limitations, and overcoming those limitations

## Slide 25: Vectorized Emulation Summary
Using Intel’s AVX-512 instructions to emulate multiple VMs in parallel on a single hardware thread
Each lane of the vector register belongs to a separate VM
Allows for faster-than-native emulation of targets
High-performance fuzzing of non-x86 targets on x86 hardware
Only useful with snapshot fuzzing
  Need to have VMs sharing the same code paths

## Slide 26: Why is this a thing?
I really wanted to get my hands on a Xeon Phi
So I bought one… had to justify it while it was shipping
Couldn’t use it for falkervisor as Knights Landing does not have VT-x
At least the memory bandwidth is fast, might be useful for emulation?
Same code bring run on multiple VMs?
  Should be able to vectorize when VMs run in lockstep

## Slide 27: What would this look like in a simple case?
Let’s say you are emulating MIPS32 and executing an `add t0, t1, t2`
  This adds the `t1` and `t2` registers and stores them into `t0`
Can we represent this using vector instructions?
  `vpaddd zmm0, zmm1, zmm2`
  Where `zmmX` holds 16 register states for the corresponding target registers `tX`
Well that was pretty easy
  Assign target architecture registers to `zmm` registers
  Each `zmm` now holds 16 32-bit VM states in parallel

## Slide 28: Would this actually work?
If all VMs execute the exact same code… this always works
  For anything meaningful, the VMs will do slightly different things
What happens on differing register states?
What happens on a memory access?
What about branches?
What about conditional branches?
  Could have an input-influenced conditional branch
  Now there is divergence between VMs

## Slide 29: Getting same code execution in VMs
Since we’re using snapshot fuzzing, each VM starts in an identical state
  All memory is the same
  All registers are the same
With the same input all VMs will do the exact same logic
  Would never have divergence in code flow
  All code would be vectorized
  No worries about differing memory accesses
Even if there is divergence, we can parallelize initialization code
  Was the initial goal of vectorized emulation

## Slide 30: What about differing register states?
Doesn’t actually matter
Two VMs executing same code with different register states
  SIMD instructions don’t care about the data
  `vpaddd` will perform the add on all the register states for the VMs, regardless of the register states

## Slide 31: Memory accesses?
Two VMs use the same instruction to access different memory
Perform a page-table walk in parallel and resolve to different memory
Read/write the memory in parallel
Not really a problem, just extra code

## Slide 32: Branches?
Just like any other JIT
Some way to look up target addresses in a table
If they’re not already JITted, then lift the target branch and insert it into the table
From this point on the lifted target is now in the target JIT table
  Target JIT table just translates target addresses to host addresses which contain the JITted code for the corresponding target code

## Slide 33: Divergent branches?
Oh… this one is actually hard
User-controlled input caused two VMs to execute different code
Cannot continue executing in parallel because different operations are now being performed?
For example, one VM goes to perform a `sub` instruction, and the other goes to perform an `add` instruction
All hope is lost?
  Nope, kmasks to the rescue

## Slide 34: AVX-512 kmask registers
Intel’s AVX-512 introduced 8 new registers, `k0` through `k7`
These mask registers can be used with any vector operation
Used to indicate which lanes to perform the operation on
Can be used in merging (preserve) or zeroing modes

## Slide 35: AVX-512 kmask zeroing example
mov k1, 0b0110
vpaddq ymm0 {k1}{z}, ymm1, ymm2
5
6
8
7
ymm1
1
2
4
3
ymm2
+
0
8
0
10
ymm0
=

## Slide 36: AVX-512 kmask merging example
5
6
8
7
ymm1
1
2
4
3
ymm2
+
31
8
7
10
ymm0
=
31
3
7
3
ymm0

## Slide 37: Making divergence possible
Emit AVX-512 kmasks for every JITted instruction
Maintain a kmask which has bits set for VMs which are executing the same code
As a VM diverges, clear the corresponding bit in the kmask
  Now that VM will not be updated while other VMs execute code
Come back to execute the VMs which were masked off at a later point
  Different ways to “come back” to VMs
    Post-dominator in the graph
    When the fuzz cases end
    Never bring them back

## Slide 38: Any more potential issues?
None that I’m aware of at this point
Let’s go actually write this!

## Slide 39: wafflecone
A 32-bit vectorized emulation implementation using Intel AVX-512

## Slide 40: Components of wafflecone
Lifters
  Converting x86/ARM/MIPS/etc to FalkIL
Intermediate language (FalkIL)
  Generic representation for all architectures
  Optimization passes and debug information to recover target state
FalkIL Interpreter
JIT
  Taking FalkIL instructions and generating AVX-512
FalkMMU
  Providing an isolated memory space for the emulated target
Not the most visually appealing program…

## Slide 41
New coverage => 00019d25
New coverage => 000198a8
vmid 0 Got crash 1337000b
Input was "229 n aZ(
"
eax 00000001 ecx b4230000 edx b4231030 ebx 0000000d
esp b4232f80 ebp b4232fe0 esi 13370009 edi b4231030
eip 00019a5e
vmid 0 Got crash 1337000b
Input was "229 �(
"
eax 00000001 ecx b4230000 edx 1337000b ebx 0000000d
esp b4232f80 ebp b4232fe0 esi 1337000b edi b4231030
eip 00019aaa
New coverage => 0001a34f
New coverage => 0001a386
uptime: 11.53 | case 778152176 | drops 1342706 | vfactor 15.9724 | fcps 77,768,824.3584 (theo 615,241,609.0636)
Restore: 0.1261 Feedback: 0.0243 Fuzz: 0.4980 VM: 0.1264 Analysis: 0.0725 Accounted cycles: 0.9358
Cov: 80 Inputs: 13121
Lifted instrs executed: 28939693248 | gips: 25032374569.55 | Avg instrs/case: 37.19 | Theo speedup 2.6869
Exit reason (VirtAddr(0xdeaddead), Branch(VirtAddr(0xdeaddead)))
Exit reason (VirtAddr(0x00019aaa), MemoryFault(ReadFault(VirtAddr(0x1337000b))))
Exit reason (VirtAddr(0x00019a5e), MemoryFault(ReadFault(VirtAddr(0x1337000b))))

## Slide 42: Lifting target code
Started with MIPS32, added PPC, ARM, x86 support later
  MIPS32 is just easier to get correct for proving the concept
Snapshot was taken on a real target
Read the memory containing the instruction pointed to by PC
Decode the instruction
  Lots of time spent reading architecture manuals
Implement the behavior of the instruction in an intermediate-language (IL)
This IL must provide all required operations to implement all target instructions

## Slide 43: FalkIL
Simple intermediate language designed for emulation
  Goal is that a new JIT or emulator implementation should take less than a day
  Allows for trying things out
  IL not designed for human readability
Ended up being about 15-20 instructions
  Add/sub/bitwise operations
  Conditional branch
  Conditional set register
  Flagless
SSA IL

## Slide 44: FalkIL Continued
RISC-like IL
No immediates on instructions
  Only a load immediate instruction
Only aligned reads and writes allowed
Explicit load/store architecture
All arithmetic instructions operate only on registers
Metadata maintained to associate IL registers with target registers
Basic optimization passes to help fuzz unoptimized code
  DCE, constant propagation, deduplication, etc

## Slide 46: JIT
Simple template-based JIT
Each IL instruction has a template for x86 vectorized code that has the same semantics
Every x86 instruction emit must have a kmask
  All JIT must respect the kmasks
  Bits clear in the kmask must result in no changes to the corresponding lane’s register or memory state
Dynamic register allocation using a mix of `zmm` registers and memory

## Slide 48: MMU
Guest memory must be organized in a way that can be vectorized
Guest memory must be isolated from host memory
  Simple software page table. JIT walks the page table on accesses
Optimized for all VMs accessing the same address
  A `vmovdqa` instruction will load a 512-bit location in memory
  Scatter/gather instructions are much more expensive
Interleave memory on 32-bit boundaries
Now if all VMs access the same address a `vmovdqa` can be used to load/store for all VMs with only one translation
Divergent loads/stores (differing addresses per VM) must go through a parallel page table walk

## Slide 49
mask 0 1 2 3
Permissions 100000000000 : 0303030303030303 0303030303030303 0303030303030303 0303030303030303
Contents 100000000000 : 34c0414141414141 34c1414141414141 34c2414141414141 34c3414141414141
Permissions 100000000008 : 0303030303030303 0303030303030303 0303030303030303 0303030303030303
Contents 100000000008 : cccccccccccccc56 cccccccccccccc56 cccccccccccccc56 cccccccccccccc56
Permissions 100000000010 : 0303030303030303 0303030303030303 0303030303030303 0303030303030303
Contents 100000000010 : 414141414141cccc 414141414141cccc 414141414141cccc 414141414141cccc
Permissions 100000000018 : 0303030303030303 0303030303030303 0303030303030303 0303030303030303
Contents 100000000018 : 4141414141414141 4141414141414141 4141414141414141 4141414141414141
Permissions 100000000020 : 0303030303030303 0303030303030303 0303030303030303 0303030303030303
Contents 100000000020 : 4141414141414141 4141414141414141 4141414141414141 4141414141414141
Permissions 100000000028 : 0303030303030303 0303030303030303 0303030303030303 0303030303030303
Contents 100000000028 : 4141414141414141 4141414141414141 4141414141414141 4141414141414141
Permissions 100000000030 : 0303030303030303 0303030303030303 0303030303030303 0303030303030303
Contents 100000000030 : 4141414141414141 4141414141414141 4141414141414141 4141414141414141
Permissions 100000000038 : 0303030303030303 0303030303030303 0303030303030303 0303030303030303
Contents 100000000038 : 4141414141414141 4141414141414141 4141414141414141 4141414141414141
Permissions 100000000040 : 0303030303030303 0303030303030303 0303030303030303 0303030303030303
Contents 100000000040 : 4141414141414141 4141414141414141 4141414141414141 4141414141414141
Permissions 100000000048 : 0303030303030303 0303030303030303 0303030303030303 0303030303030303
Contents 100000000048 : 4141414141414141 4141414141414141 4141414141414141 4141414141414141
Permissions 100000000050 : 0303030303030303 0303030303030303 0303030303030303 0303030303030303
Contents 100000000050 : 4141414141414141 4141414141414141 4141414141414141 4141414141414141

## Slide 50: MMU Hardening
We want ASAN/uninitialized protections
Every byte of guest memory has a byte of permissions
Permission byte has explicit read, write, execute, and RAW bits
Out-of-bounds access by 1-byte causes a fault
  Technically stronger than ASAN
Read-after-write (RAW) bit
  Set if memory should be readable, but only after it has been written once
  New allocations in the guest set as RAW
  Fault will occur if the memory is read before written
  Uninitialized memory use detection, with byte-level granularity

## Slide 51: Code Coverage
With a JIT code coverage is easy
Code is only ever JITted when it’s hit
Code coverage is just the size of the JIT database
  Might need custom hooks if PC/edge/block/graph coverage is desired
For finer-grained coverage just emit JIT to update a global bitmap

## Slide 52: Differential Coverage
Only saving coverage based on user-controlled divergence

## Slide 53: Horizontal Comparison
Running with 16 other VMs in parallel
Can cheaply “look to your neighbor” to determine if you’re doing something new
  On conditional and indirect branches, check what your neighbors are up to
  If they’re going somewhere else than where you are, something changed in the input caused this change
  Save the input for future use
  With a smart fuzzer, prioritize the operation you performed as a meaningful one
    Associate changes and mutation strategies with what they affected in the program state

## Slide 54: Horizontal Comparison Implementation
1
4
4
3
ymm0
4
4
4
4
ymm1
Broadcast bottom word of ymm0 to ymm1
Vector compare between ymm0 and ymm1 into mask k2
0
1
1
0
k2
If k2 is not equal to the online mask, user input influenced this value!

## Slide 55: Memory/Register State Coverage
Typically not feasible due to storage overhead
  Need to log every register on every instruction
Track unique register and memory states observed during fuzzing
  Just like code coverage, but tracking program states
Goal is to get coverage information for state machines
  Same code, different states, potentially crashes in “common” code paths
Vectorized Emulation makes it feasible
  On register/memory loads/stores look to your neighbors
  If they have a different value, log the input as a new one
  Coverage is only gathered on instructions which user input influences
  No tracking register state on uncontrolled `printf()` state

## Slide 56: Divergent Coverage
Only store coverage information when it was caused by user-inputs
Coverage databases only hold user-controlled branch information
  Reduces memory required to store databases
  More meaningful information for human consumption
Can track when user-controlled data affected a register state or memory state
  Don’t know “why” it was affected, but you know that it was
  Can color IDA to show hit code, influenced register writes, and influenced register reads

## Slide 57: Divergence

## Slide 58: Results

## Slide 59: Results
Sadly limited usage
  I’ve just been busy
Fuzzed Windows and OpenBSD DHCP servers and client
  Trillions of fuzz cases per week in each
  Over 20 unique bugs in Windows DHCP
    6+ RCE bugs
    Re-finds all 20 bugs in under 5 minutes of runtime
  1 silly OpenBSD bug
    Out-of-bounds read in the highest level for loop
    Almost always incorrect
    Wouldn’t have found without byte-level
1 remote bluescreen in Windows Firewall code

## Slide 60: Solving-like Behavior
Register and memory coverage with feedback yields… strange results
Un-enlightened byte-flipper can find valid inputs
let fuzz_input = corpus.random_input();
for _ in 0..rng.xorshift() % 4 {
let offset = rng.xorshift() % fuzz_input.len();
let byte = rng.xorshift() as u8;
for vmid in vm.online() {
let fuzz_input = &mut fuzz_input[vmid];
fuzz_input[offset] = byte.wrapping_add(vmid as u8);
}
}

## Slide 62: Stress testing coverage
Created Hellscape, a proving ground for coverage guided fuzzers
https://github.com/gamozolabs/hellscape
Has multiple bugs reachable with coverage guided fuzzers
  Branch-per-byte-comparison (findable with code coverage, AFL)
  memcmp()-like comparison (register coverage)
  Multiple memcmp()-like comparison (path based register coverage)
  Batched memcmp()-like comparison (register coverage, word shattering)
  Multiple batched memcmp()-like comparison (path based register coverage, word shattering)
All bugs should be findable with a byte flipper, no enlightenment
wafflecone finds all 5 bugs in under a second

## Slide 63: Conclusion

## Slide 64: Should you use vectorized emulation?
Probably not
It’s too fast
  For small targets it runs over a million fuzz cases per second
    Getting meaningful fuzz inputs a million times a second is a hard problem
Probably better things to do with your time
  Switch to a coverage-guided fuzzer
  Use coverage in a meaningful way
  Write a new fuzzer to the specification you’re fuzzing
  Audit code!
  Switch to snapshot fuzzing
  Still have done all of these things? Still need more bugs? Okay maybe use vectorized emulation

## Slide 65: Questions?